## Slide 1: Cross-Country for Beginners Part 5: Flight Computers and Final Glides
Bill Elliott and Rand Baldwin

## Slide 2: Tonights Topics
Final Glides (getting to emergency fields)
Flight Computers and what they can do for you
Flight Analysis
Summary

## Slide 3: Final Glides
What we really need to know is not “How much altitude to I need to reach an airport?”
What we realy need to know on a continual basis is “What can I reach from where I am now?”
We do too much “estimating” in our heads
This leads to lots of “fudge factors”
Which reduces what think we can do
Limiting what we can do
Which just paralyzes us psychologically!

## Slide 4: You ask, “How Far Can I Glide?”
I prefer this calculation which gives glide distance in nautical miles per thousand feet of altitude:
Glide Ratio / 5 = Glide Distance in sm
or, for the Astir CS
35 / 5 = 7 sm, roughly
This comes from:
35 * 1000 ft of Alt = 35,000 ft of Distance
= 35,000 ft / 5,280 ft / sm
= 35 / 5.3 = 6.6 sm
or
= 36/ ~5 = ~ 7sm – easier math!

## Slide 5: What about safety margin?
Degrade you best L/D by ~10% (or whatever you like):
so, for something like the Astir
35 – 4 = 31
therefore
31 / 5 = 6 sm
and, for the Blanik
30 – 20% = 24
therefore
24 / 5 = ~5 sm with a 20% margin, so you can get back from Mad Co Lake from 2,600 agl

## Slide 6
Six Mile Circle
Adding concentric rings

## Slide 7: Required Altitude for Best L/D = 30:1
10 miles
8
6
4
2
0
1,000
2,000
3,000
500 ft
1,000
1,500
1,000 ft Pattern Altitude
Plus 500 ft Safety Margin
30 / 5.28 = 5.68 miles per 1000 ft
or
176 ft per mile , therefore
1,760 per 10 miles.
Given a 1,000 ft pattern plus 500 ft safety
You need ~3,300 ft to go 10 miles.
At 2,500 ft, you can go about six miles.

## Slide 8
Add more landable fields
Six Mile Circles

## Slide 9: Required Altitude for Best L/D = 30:1
10 miles
8
6
4
2
0
1,000
2,000
3,000
500 ft
1,000
1,500
500 ft Pattern Altitude
Plus 500 ft Safety Margin
Given a 500 ft pattern plus 500 ft safety
You need ~2,800 ft to go 10 miles.
At 2,500 ft, you can go about eight miles.

## Slide 10
Eight Mile Circles

## Slide 11: What if Best L/D more like 35:1?
10 miles
8
6
4
2
0
1,000
2,000
3,000
Astir CS MC Sink Rate Req’d Alt
No wind 0 1.3 1,430
500 ft
1,000
1,500
500 ft Pattern Altitude
Plus 500 ft Safety Margin
Given a 500 ft pattern plus 500 ft safety
You need ~2,500 ft to go 10 miles.
At 2,500 ft, you can go about ten miles.

## Slide 12
Ten Mile Circles

## Slide 13: What’s the point?
Oh my god … some many circles!
We have been trained to think along these terms:
  What is my glide ratio?
  How far can I go?
  Can I get to an airport or a landable field?
  What if the wind quits?
All of this thinking, figuring, analyzing paralyzes us.
We can do better

## Slide 14: Why Cruise Faster than Best L/D?
10 miles
8
6
4
2
0
1,000
2,000
3,000
Astir CS MC Sink Rate Req’d Alt
0 1.3 1,430
No wind 1 1.6 1,510
2 2.1 1,680
3 2.6 1,880
500 ft
1,000
1,500
400+ ft
margin
MC = 3, Cruise 5 miles, now 250 below glide.
Simple adjust MC = 1 and your back on glide.
500 ft Pattern Altitude
Plus 500 ft Safety Margin
MC solution is shortest time home.
MC provides altitude “in the bank”.
This MC “bank account” scales with distance.
Maybe you encounter sink.

## Slide 15: What about Incorrect Wind?
10 miles
8
6
4
2
0
1,000
2,000
3,000
500 ft
1,000
1,500
Astir CS MC Sink Rate Req’d Alt
0 1.3 1,810
+10 wind 1 1.6 1,830
2 2.1 1,980
3 2.6 2,180
Cruise 4 miles MC = 3, now 250 below glide.
No sense of going through sink, must be the wind.
Adjust the headwind component in Flight Computer.
Not all flight computers get the wind right,
but off by 10 knots is a huge error and is unlikely.
Now adjust MC = 2 and your back on glide.
Was 1,880

## Slide 16: Now what’s the point?
Oh my god … some many glide slope lines … and sink … and wind errors!
Now how do we do all that figuring for:
  What is my glide ratio?
  How far can I go?
  Can I get to an airport or a landable field?
  What if the wind quits?
You don’t, that’s the point, you get a flight computer.
And … you learn to use and learn to believe it!

## Slide 17: What if you had a Flight Computer
Your in the Astir
Your at 2,600 ft
Wow! You know a lot!
Sense of paralysis is gone!
Location is known
Performance known
Wind known
Airports known
Landable fields known

## Slide 18: Let’s talk Flight Computers
You need one, period.
What kind you get is up to you and your budget.
Let’s go over some Pro’s and Con’s for:
  Low Cost Systems
  Medium Cost Systems
  High End Systems

## Slide 19: PDA and PNA based Systems
Pros
  High speed processor
  Graphical display
  Color
  Touchscreen
  Rapid technology upgrades
  Wide variety of software available
  Free Software development tools
Cons
  Screens not as easy to read as in panel displays in sunlight
  Depending on mounting solution, can get in the way of view out canopy or block access to controls
  Internal Batteries won’t last when communicating with a GPS, so a 5 V power converter is required (some instruments provide 5 V)

## Slide 20: Glide Navigator II
Pocket PC
Programmers: Chip Garner, Rich Herr
Marketing and Support: Paul Remde
$200
Designed for ease-of-use in flight
Big “finger sized” buttons and large display text
Simple, uncluttered map display – only the information you need to fly your task
Easiest to learn for a non-technical person
Popular

## Slide 21: Low Cost Systems
Components
  Pocket PC or Palm OS PDA
  GPS
  Cables and Power Supply for PDA (5 V) and GPS (12 V or 3.3 V)
$290 to $1200
Example Systems
  Glide Navigator II on Dell Axim X5 with Transplant CF Card GPS
  Any soaring flight software on any PDA
  GPS Types
    CF Card
    SDIO GPS
    “Puck” style
    BlueTooth GPS
    Garmin or similar

## Slide 22: What Low Cost Systems Can Do
Use GPS Position and Altitude
Moving Map with Waypoints and SUA
Final Glide Calculations
Reachable Airports Highlighted
Record Unofficial IGC flight logs
Tasks
Portable (suction cup mount)
No cables (depending on GPS)
Flight Statistics
GPS altitude used for final glide (not best)
OK for some contests?
Improved safety through quick access to final glide data
Wind speed and direction calculated using drift while circling
90% of what the high cost systems can do

## Slide 23: What Low Cost Systems Can’t Do
No Pressure Altitude Data
No IGC Approved flight log for badges and records
No Vario or averager
No Speed-to-fly
Can’t calculate wind speed and direction using airspeed and GPS data while cruising
When used with a speed-to-fly vario you must enter MacCready into both devices

## Slide 24: Low Cost Systems
Components
  Pocket PC or Palm OS PDA
  GPS
  Cables and Power Supply for PDA (5 V) and GPS (12 V or 3.3 V)
$290 to $1200
Example Systems
  Glide Navigator II on Dell Axim X5 with Transplant CF Card GPS
  Any soaring flight software on any PDA
  GPS Types
    CF Card
    SDIO GPS
    “Puck” style
    BlueTooth GPS
    Garmin or similar

## Slide 25: What Medium Cost Systems Can Do
Use GPS Position and Pressure Altitude
Moving Map with Waypoints and SUA
Final Glide Calculations
Reachable Airports Highlighted
Record IGC Approved flight logs
OK for all contests, badges, and records
Tasks
Flight Statistics
Improved safety through quick access to final glide data
Wind speed and direction calculated using drift while circling
Portable - maybe
92% of what the high cost systems can do

## Slide 26: What Medium Cost Systems Can’t Do
No Vario or averager
Minimal Speed-to-fly
Can’t calculate wind speed and direction using airspeed and GPS data while cruising
When used with a speed-to-fly vario you must enter MacCready into both devices

## Slide 27: SeeYou Mobile and LX Nano
Oudie with internal GPS
Price: $650
Moving map very configurable
Statistics pages
Thermal history page
Topographical maps – same maps used in SeeYou for PC
Shaded area for FAI triangles
Online Contest competition calculation in flight
Need an IGC-approved GPS/ logger
No variometer

## Slide 28: High End Systems
Components
  Vario with audio and averager
  IGC Approved Flight Recorder with GPS
  LCD Display in instrument panel, or PDA
$3000 to $5000
Example Systems
  CAI 302 plus Glide Navigator II
  ClearNav plus Vario and logger
  ILEC SN-10 with vario plus GPS logger
  LX8000 with vario and logger
  Zander with vario and logger

## Slide 29: What High End Systems Can Do
Vario with Audio and Averager
Speed-to-fly director
Wind speed and direction calculated using airspeed and GPS data while circling or cruising
Use GPS Position and Pressure Altitude
Moving Map with Waypoints and SUA
Final Glide Calculations
Reachable Airports Highlighted
Record IGC Approved flight logs
OK for all contests, badges, and records
Tasks
Flight Statistics
Improved safety through quick access to final glide data
MacCready only entered once on vario or PDA and data shared between devices

## Slide 30: What High End Systems Can’t Do
Not much …
But, they are expensive!

## Slide 31: Example High End Systems
Ilec SN-10B - $2295
LX Nano - $890
Cable - $45
Total: $3230
Unique Features
  Exclusive Thermal Height-Band Graph
  No PDA required
  Landing fields on map screen in new version this spring
  absolute minimal heads-down time
  the best wind measurement system flying (with graphic wind arrow)
  the best vario available with excellent (non-irritating) audio
  quick, intuitive information presentations
  pilot-friendly controls (left-hand remote doesn't interfere with flying)
  concise moving-map display of task and airspace
  very high-contrast display with minimal clutter
  painless final-glides around turnpoints (with accurate remaining-time-til-finish)
  custom page
  reliable software, hardware, and manufacturer - NO SOFTWARE CRASHES
  usable in flight, not just your living room

## Slide 32: Flight Analysis
Buy SeeYou … everyone uses it so you can get help and it integrates with SYM
Analyze your flights, every flight.
Do like we did and look carefully at your climbs and your glides
Then, look closely at the barogram
  What do the climbs look like?
    Climb should be steady, no rollover to the right.
    Look at how you exit, no rounded tops
    Look at you use of the heightband
  What does the cruise look like?
Finally, look closely at the stat.
  Average climb rate and percent time climbing
  Number of tries
  Average cruise length and at what avg IAS
  Time in rising air vs sinking air
  Avg L/D achieved

## Slide 34
Rounded Top
Rollover
Huh?

## Slide 36: Let’s look at this trace …

## Slide 37: That’s all folks!
Let’s start planning the leader-follower flying sessions.